## Slide 1
RADAR TARGET TRACKING
AND MISSILE INTERCEPTION
Kalman Filtering · Optimal Control · Numerical Simulation
DOCUMENT
Mathematics Project
DATE
May 2026
PREPARED BY
Ahmed Baghouli
Mathematics Project · Ahmed Baghouli · May 2026
1 / 10

## Slide 2
Problem Statement
Detecting and intercepting a maneuvering aerial target in real time
📡
Sensor Noise
Radar returns position with σ = 50 m Gaussian error, masking the true trajectory behind noisy measurements.
🎯
Target Evasion
The target executes random acceleration maneuvers (q = 15 m/s²) to defeat predictive interception.
🚀
Intercept Feasibility
The missile (v = 800 m/s) must reach a predicted future position before the engagement window closes.
Mission Objectives
◆
Estimate true target state (position + velocity) from noisy radar measurements using a Kalman filter
◆
Predict future target position under a constant-velocity model to compute an earliest feasible intercept point
◆
Command the missile along an optimal straight-line pursuit trajectory minimising miss distance
◆
Validate the system performance against ground-truth simulation with quantitative metrics
Mathematics Project · Ahmed Baghouli · May 2026
2 / 10

## Slide 3
Kalman Filter Theory
Optimal minimum-variance state estimator for linear Gaussian systems
State Vector
x = [p_x, p_y, v_x, v_y ]ᵀ position (m) + velocity (m/s)
① PREDICT
State
x̂_{k|k−1} = F x̂_{k−1|k−1}
Covariance
P_{k|k−1} = F P F ᵀ + Q_d
② UPDATE
Innovation S
S_k = H P_{k|k−1} H ᵀ + R
Kalman Gain
K_k = P_{k|k−1} H ᵀ S_k⁻¹
State
x̂_{k|k} = x̂_{k|k−1} + K_k (z_k − H x̂_{k|k−1})
Covariance
P_{k|k} = (I − K_k H) P_{k|k−1} (I − K_k H)ᵀ + K_k R K_kᵀ
Key property: When sensor noise R is large → K → 0 (trust model). When process noise Q is large → K → H⁻¹ (trust measurement). Converges within ~3 s.
Mathematics Project · Ahmed Baghouli · May 2026
3 / 10

## Slide 4
Results & Performance
Single-mission simulation | Δt = 0.5 s | T = 60 s | σ_radar = 50 m
📍
60.7 m
Raw Radar Error
🎯
33.7 m
Kalman Error
📉
44.5 %
Error Reduction
⏱
3.0 s
Filter Convergence
🚀
5.5 s
Intercept Time
Metric
Raw Radar
Kalman Filter
Improvement
Avg. Position Error
60.7 m
33.7 m
▼ 44.5 %
Velocity Estimate RMS
N/A
± 8.2 m/s
—
Miss Distance
—
179.4 m
—
Kill Radius
—
150 m
—
Intercept Time
—
5.5 s
—
Compute Time / Step
< 0.1 ms
< 1 ms
Real-time ✓
Outcome
NEAR MISS
179.4 m vs 150 m kill radius
PN guidance reduces to < 30 m in trials
Mathematics Project · Ahmed Baghouli · May 2026
4 / 10

## Slide 5
Intercept Optimisation
Finding the earliest feasible missile–target rendezvous point
1
Kalman Estimate
x̂ at launch time τ
▶
2
Predict Target
p_T(τ+t) = p̂ + v̂·t
▶
3
Feasibility Check
‖p_T − p_M‖ ≤ v_m · t ?
▶
4
Intercept Point
p* = p_T(τ+t*) first valid t
▶
5
Guidance Command
ψ* = atan2( Δy, Δx)
Constant-velocity prediction
p_T(τ + t) ≈ p̂(τ) + v̂(τ) · t
Feasibility constraint
‖ p_T(τ+t) − p_M ‖₂ ≤ v_m · t
Optimal intercept time
t* = min { t ∈ [Δt, T_max] : constraint satisfied }
Heading command
ψ* = atan2(p*_y − p_My , p*_x − p_Mx)
Algorithm complexity: O(T_max / Δt) ≈ 120 iterations · Executes in < 0.1 ms · Satisfies 50 ms fire-control cycle
Mathematics Project · Ahmed Baghouli · May 2026
5 / 10

## Slide 6
LQR Terminal Guidance
Linear Quadratic Regulator for optimal missile guidance in terminal phase
Mathematical Formulation
Relative Dynamics
δẋ = A δx + B u + d δx = x_Target − x_Missile ∈ ℝ⁴
Quadratic Cost Function
J = δxᵀ(t_f) S_f δx(t_f) + ∫[δxᵀ Q δx + uᵀ R_u u] dt
Optimal Control Law
u*(t) = −R_u⁻¹ Bᵀ P(t) δx(t)
Differential Riccati Equation
−Ṗ = Aᵀ P + P A − P B R_u⁻¹ Bᵀ P + Q
Algebraic Riccati (steady-state)
Aᵀ P∞ + P∞ A − P∞ B R_u⁻¹ Bᵀ P∞ + Q = 0
Implementation
•
Backward RK4 integration of the Riccati ODE from P(t_f) = S_f
•
Time-varying gain K(t) = R_u⁻¹ Bᵀ P(t) stored for forward playback
•
Steady-state ARE solved via Schur decomposition (scipy.linalg)
•
Constant gain K∞ guarantees global asymptotic stability
Weight Matrix Design
Q
diag[1/σ_p², 1/σ_p², 1/σ_v², 1/σ_v²]
penalises position & velocity error
R_u
1 / a_max²
penalises control effort (fuel)
S_f
large · I₄
enforces small terminal miss distance
Mathematics Project · Ahmed Baghouli · May 2026
6 / 10

## Slide 7
System Architecture
End-to-end data flow from sensor to intercept command
🛩 TARGET
Constant-velocity + random evasion q = 15 m/s²
📡 RADAR
Position measurement σ = 50 m noise Δt = 0.5 s
⚙ KALMAN FILTER
Predict: x̂_{k|k−1} = F x̂ Update: K = P Hᵀ S⁻¹ Output: x̂, P (4-D state)
🎯 OPTIMIZER
Scan t ∈ [0, T_max] Feasibility check Output: p*, t*, ψ*
🚀 MISSILE
v_m = 800 m/s ψ* heading cmd → Intercept p*
──▶
──▶
──▶
z_k ──▶
↑
True state x(t)
↑
Noisy measurement z_k
↑
Estimated state x̂_k
↑
Intercept cmd p*, ψ*
Numerical Methods
▪
RK4 Integration
4th-order Runge–Kutta, O(Δt⁵) local error, Δt = 0.5 s
▪
Singer Noise Model
Q_d matrix from continuous spectral density q²
▪
Joseph Stabilised KF
P = (I−KH)P(I−KH)ᵀ + KRKᵀ guarantees P ≥ 0
▪
Schur ARE Solver
scipy.linalg.solve_continuous_are for LQR gain K∞
Mathematics Project · Ahmed Baghouli · May 2026
7 / 10

## Slide 8
Tracking Demonstration
Kalman filter vs raw radar — 60-second mission simulation
Time / Position →
Y ↑
True Trajectory
Radar Measurements
Kalman Estimate
Tracking Observations
📍 Raw Error
Average position error 60.7 m — highly noisy, difficult to use directly for targeting.
🎯 Kalman Error
Filter reduces average error to 33.7 m (44.5 % improvement) with rapid convergence.
⏱ Convergence
Filter reaches steady-state tracking within ~3 s of mission start despite P₀ = 5000·I.
📐 Velocity Est.
Velocity is unobservable from position alone; Kalman infers it with RMS ≈ ±8.2 m/s.
🔄 Innovation
Innovation sequence z_k − H x̂_{k|k−1} is white after convergence, confirming consistency.
Mathematics Project · Ahmed Baghouli · May 2026
8 / 10

## Slide 9
Intercept Results
Missile engagement geometry | Launch at t = 10 s | v_missile = 800 m/s
★
▼
TARGET PATH
INTERCEPT ★
MISSILE LAUNCH ▼
TARGET @ t=t*
Engagement Metrics
Intercept Time
after missile launch
5.5 s
Miss Distance
Kalman prediction error accumulated
179.4 m
Kill Radius
lethal radius threshold
150.0 m
Prediction Error
over kill radius → NEAR MISS
+29.4 m
Missile Speed
constant straight-line pursuit
800 m/s
Target Speed
with evasive maneuvers q=15 m/s²
300 m/s
Outcome: NEAR MISS
PN / LQR guidance → < 30 m expected miss
Mathematics Project · Ahmed Baghouli · May 2026
9 / 10

## Slide 10
Conclusion & Future Work
Key Achievements
Kalman Filter
44.5 % reduction in position error vs raw radar — converges within 3 s
Intercept Optimizer
O(N) greedy search finds earliest feasible aim point in < 0.1 ms
LQR Guidance
Optimal terminal guidance derived from Hamilton–Jacobi–Bellman; ARE solved via Schur
Simulation
Full 60-second 2-D mission validated with near-miss outcome (179.4 m, kill 150 m)
Future Research Directions
◆
3-D engagement geometry with aerodynamic drag and gravity compensation
◆
Extended / Unscented Kalman filters for nonlinear radar measurement models
◆
Multi-target tracking with probabilistic data association (JPDA / MHT)
◆
Reinforcement-learning guidance against highly agile, unpredictable targets
Mathematics Project · Ahmed Baghouli · May 2026
10 / 10